## Slide 1: ArUco Tag Follower
Lucas Plant, Will Langley, Kanussh Jain, John Matthews

## Slide 2: Intended Behavior
Use “Visual Servoing” to have the manipulator follow an object
Bring ArUco tag into view
Move ArUco tag
End effector moves with 2 objectives
  Keep the ArUco tag in view of the camera using rotation
  Follow the position of the tag (with an offset) using translation

## Slide 3: Procedure
Sample a frame from the camera
Compute the difference in the ArUco tag orientation and the current orientation
Use forward kinematics to derive pseudo-inverse Jacobian
Use resolved rate to determine the next joint angles
Move to the desired joint angles
Repeat with next frame

## Slide 4: Resolved Rate for Visual Servoing
Determine target twist in the end effector or camera frame based on the error
Move in the direction of the desired twist using the damped inverse jacobian

## Slide 6: Technical Challenges
Low camera quality
  Motion blur
  Frame rate
  Rolling vs global shutter
  Jerky movement
  Losing tag from movement
  Pose resolution was slow restricting control rate
Kinematic constraints of the robot
  Full pose tracking is impossible as the requested pose may be outside of the workspace
  Specifically yaw is impossible due to lack of wrist swivel
  Instability due to gains

## Slide 7: Thank You for Listening!
https://youtu.be/sU2IApv3Ekg?si=8Va_pyqXZPuSU5c5